## Slide 2
PWM Signal:
Ramp Input from 1000us to 2000us
Motor RPM:
Ramp Input from 1000us to 2000us -> 2 Cycles
Saturation
Rpm variation (51-53)
PWM ([1000, 1100], [1800, 2000])
ESTIMATION DATASET
Region of Interest
PWM([1100 , 1400], [1500, 1800])
DEAD BAND
PWM(1410 -1490)

## Slide 3
DATA FILTERING
As the region of interest lies in [1100us, 1400us] for clockwise motion and [1500us, 1800us] for anticlockwise motion, thus here we only filter the data points from the above region and rescale the input signal so as to make the above region a continuous function.
Region 1 : - [1100us, 1400us] (clockwise)
New Scale: [-300, 0]
Subtract the PWM signal by 1400
Region 2 : - [1500us, 1800us](anti-clockwise)
New Scale: [0, 300]
Subtract the PWM signal by 1500
The Input to the plant will be sent with respect to the new scale.
REGION 1
REGION 2

## Slide 4
SYSTEM IDENTIFICATION
TOOLBOX
Poles: 1 Zeros: 0
Number of poles: 1 Number of zeros: 0
Status:
Fit to estimation data: 75.87%
FPE: 90.42, MSE: 86.49

## Slide 5
SYSTEM IDENTIFICATION
TOOLBOX
Poles: 2 Zeros: 0
Number of poles: 2 Number of zeros: 0
Status:
Fit to estimation data: 93.3%
FPE: 7.172, MSE: 6.66

## Slide 6
SYSTEM IDENTIFICATION
TOOLBOX
Poles: 2 Zeros: 1
Number of poles: 2 Number of zeros: 1
Status:
Fit to estimation data: 91.33%
FPE: 12.2, MSE: 11.16

## Slide 7
SYSTEM IDENTIFICATION
TOOLBOX
Poles: 2 Zeros: 2
Number of poles: 2 Number of zeros: 2
Status:
Fit to estimation data: 93.35%
FPE: 7.284, MSE: 6.566

## Slide 8
SYSTEM IDENTIFICATION
TOOLBOX
Poles: 3 Zeros: 1
Number of poles: 3 Number of zeros: 1
Status:
Fit to estimation data: 84.3%
FPE: 41.22, MSE: 36.61

## Slide 9
SYSTEM IDENTIFICATION
TOOLBOX
Poles: 3 Zeros: 2
Number of poles: 3 Number of zeros: 2
Status:
Fit to estimation data: 93.3%
FPE: 7.62, MSE: 6.668

## Slide 10
PWM Signal:
Ramp Input from 700us to 1400us
Motor RPM:
Ramp Input from 700us to 1400us
-> Clockwise rotation (RPM +ve)
Saturation
Rpm variation (51-53)
PWM (700 - 1100)
VALIDATION DATASET - 1
Region of Interest
PWM(1100 - 1400)
CLOCKWISE RUN

## Slide 11
PWM Signal:
Ramp Input from 1400us to 2300us
Motor RPM:
Ramp Input from 1400us to 2300us
-> Anticlockwise rotation (RPM -ve)
Saturation
Rpm variation (51-54)
PWM (1800 - 2300)
VALIDATION DATASET - 2
Region of Interest
PWM(1100 - 1400)
ANTICLOCKWISE RUN
DEAD BAND
PWM(1410 -1490)

## Slide 12
PWM Signal:
Ramp Input from 1400us to 2300us
Motor RPM:
Ramp Input from 1400us to 2300us
-> Anticlockwise rotation (RPM -ve)
Saturation
Rpm variation (51-54)
PWM (1800 - 2300)
VALIDATION DATASET - 3
Region of Interest
PWM(1500 - 1800)
ANTICLOCKWISE RUN
DEAD BAND
PWM(1410 -1490)